## Slide 1: Atmospheric Aerosols and Health Effects
ES-06: Introduction to Environmental Science and Engineering
February 18, 2021
Notes: missing – aerosol climate effects

## Slide 2: Outline
Health impacts of air pollution
Source attribution and lifetimes of aerosols in the atmosphere
Trends in control/exposures

## Slide 3
What is "PM2.5"
(…PM 10, PM1, ….)
PM2.5 means particulate matter with an aerodynamic diameter less than or equal to a nominal 2.5 micrometers (mm) as measured by an EPA reference or equivalent method†.
PM2.5 particles are known to produce respiratory and cardiovascular illness, as well as systemic inflammation. They are small enough to invade even the smallest airways. These particles generally come from activities that burn fossil fuels, such as traffic, smelting, and metal processing.
Particulate air pollution can cause inflammatory responses in the body's respiratory tract and in the blood vessels, and nerve channels.
† based on 40 CFR Part 50 Appendix L and designated in accordance with 40 CFR Part 53 or by an equivalent method designated in accordance with 40 CFR Part 53.

## Slide 4: Health Impacts of Particulate Matter
Goudie and Middleton, 2006
…and moves throughout the body.
Notes: air pollution is operationally defined – impact is really a function of chemical composition and surface properties; gets into the deepest parts of the lung … and does not stay there !!

## Slide 5
Blood
Altered rheology
Increased coagulability
Translocated particles
Peripheral thrombosis
Reduced oxygen saturation
Systemic Inflammation
Oxidative Stress
Increased CRP
Proinflammatory mediators
Leukocyte & platelet activation
PM Inhalation
Brain
Increased cerebrovascular ischemia
Heart
Altered cardiac
autonomic function
Increased dysrhythmic susceptibility
Altered cardiac repolarization
Increased myocardial
ischemia
Vasculature
Atherosclerosis,
accelerated progression of and destabilization of plaques
Endothelial dysfunction
Vasoconstriction and Hypertension
Lungs
Inflammation
Oxidative stress
Accelerated progression
and exacerbation of COPD
Increased respiratory symptoms
Effected pulmonary reflexes
Reduced lung function
There are multiple mechanistic pathways that have complex interactions and interdependencies.
Particles travel in the body!

## Slide 6
Very small particles (ultrafine, nuclei) efficiently enter into cells across the cell membrane by endocytosis mechanisms
Notes: Cellular Uptake of Nanoparticles: Journey Inside the Cell
Shahed Behzadi, Vahid Serpooshan, Wei Tao, Majd A. Hamaly, Mahmoud Y. Alkawareek, Erik C. Dreaden, Dennis Brown, Alaaldin M. Alkilany, Omid C. Farokhzad, Morteza Mahmoudi
Chem Soc Rev. Author manuscript; available in PMC 2018 Jul 17.

## Slide 7: In the news…
The world’s most polluted megacity:
PM2.5 = >150 g m-3
US Standard: 15 g m-3
“Unhealthy”: 100 g m-3
Health effects observed: 8 mg-3
https://www.newyorker.com/culture/personal-history/raising-kids-in-delhis-worsening-air
How do we know that health effects occur: people in cities… (or rats or rabbits in a chamber );
follow people for 3 decades.
Notes: How do we know that health effects occur: people (or rats) in a chamber; follow for 3 decades

## Slide 8
Many populous counties experience 40-150% increases in smoke concentrations in summer.
Much of California sees a doubling of “smoke waves” – episodes of enhanced smoke at the 98th% level.
Harvard researchers are investigating the health consequences of greater smoke.
Wildfires may increase in the 2050s atmosphere, leading to large enhancements in smoke particles.
Percent increase in smoke PM2.5 by midcentury relative to 2000s, by county.
Some large cities affected by fires
Liu et al., 2016
connect to climate issue:
soil moisture,
T extremes,
precipitation,
snow melt
Notes: connect to climate unit: soil moisture, connection to climate

## Slide 9: Air Pollution: Spans wide spatial and temporal scales
Global
Regional
100-1000 km
Acid Rain
Global Climate
Ozone Depletion
Urban Pollution
Indoor Air
Local
<100 km
Spatial
Notes: Why are these scale-dependent interactions important ?? global climate effects are later

## Slide 10
●
CO Concentration (ppb)
Black Carbon ng/m3
Notes: Add Harvard Forest and MLO temporal

## Slide 11
Where is PM1 ? Why isn't PM1 a Criteria Pollutant?
Notes: Why is PM-1 missing – students.

## Slide 12
Particle Size
Distributions in the
Environment:
Different for
number, surface area
and volume (mass)
10 100 nm

## Slide 13
Pyramid of Effects of Air Pollution
13
Death
Doctor Visits,
School Absences,
Lost Work Days
Respiratory Symptoms,
Medication Use,
Asthma Attacks
ER Visits,
Hospital Admissions,
Heart Attacks
Lung Function Decrements,
Inflammation, Cardiac Effects
Severity of Effect
Magnitude of Impacts
Thousands
Tens of Thousands
Millions
Hundreds of Thousands
Adapted from US EPA
Annually in US:
O3 and PM2.5 make up majority of air pollution health burdens
Estimated cost:
Hundreds of billions

## Slide 14
Weather conditions strongly affect pollution levels where people live.

## Slide 15: Key Features of London Fog Event (1952)
US NAAQS PM standards
US NAAQS:
PM2.5 = 0.012 mg m-3
PM10 = 0.150 mg m-3
SO2
NOx
An inactive person inhales about 10 m3/day

## Slide 16: Five minute discussion topic
Estimate the number of people who died as a result of the pollution event
2020-03-03

## Slide 18: 6 Cities Study (Dockery et al., 1993)
http://www.nejm.org/doi/full/10.1056/NEJM199312093292401
Mortality
P = Portage, Wisconsin
T = Topeka, Kansas
W = Watertown, Massachusetts
L = St. Louis
H = Harriman, Tennessee
S = Steubenville, Ohio
n = ～ 1200 to 1600 individuals per city

## Slide 19: Outline
Health impacts of air pollution
Source attribution and lifetimes of aerosols in the atmosphere
Trends in control/exposures

## Slide 20
AOD: Aerosol optical depth – dz
(r is the effective particle radius for light scattering)

## Slide 21: 1. Examples of types of particles
Particles contrails provide a nucleus upon which cloudwater condenses.
Pollution off U.S. east coast
Black carbon
California fire plumes
Light-colored particles reflect sunlight and cool the earth’s surface.
cooler
2. Examples of how particles affect climate.

## Slide 22
Life cycle of particulate matter (PM, aerosols)
Secondary Particles are formed from gases that are oxidized or create acid-base pairs
nucleation
coagulation
condensation
.
.
.
.
.
.
cycling
ultra-fine
(<0.01 mm)
fine
(0.01-1 mm)
cloud
(1-100 mm)
scavenging
precursor gases
Soup of chemical reactions
evaporation
(10-3 – 10-4 mm)
Precursor gases:
SO2, NH3, NOx, organic gases (“VOCs”)
↓↓↓ atmospheric chemical reactions, uptake by existing particles
Secondary particle components:
Sulfate, ammonium, nitrate, partially oxidized organics
sunlight

## Slide 23: Life cycle of particulate matter (PM, aerosols)
nucleation
coagulation
condensation
wildfires
soil dust
.
.
.
.
.
.
cycling
ultra-fine
(<0.01 mm)
fine
(0.01-1 mm)
cloud
(1-100 mm)
combustion
volcanoes
agriculture
biosphere
coarse
(1-10 mm)
scavenging
precursor gases
Some particles are emitted directly, some form from gases in the air.
Soup of chemical reactions
NOx
NOx
NOx
NOx
NOx
VOCs
VOCs
VOCs
VOCs
VOCs
SO2
NH3
SO2
evaporation
sea salt
(10-3 – 10-4 mm)
Life cycle of particulate matter (PM, aerosols); Primary aerosols are emitted directly
Secondary Particles, formed from gases that are oxidized or create acid-base pairs
Primary particles: soot, metals, sea salt, dust, ash, smoke – usually coarse mode
sunlight
Notes: re-create this slide; primary and secondary; SOA

## Slide 24: Outline
Health impacts of air pollution
Source attribution and lifetimes of aerosols in the atmosphere
Trends in control/exposures

## Slide 25: Before the U.S. Clean Air Act (1970/1990)
North Birmingham, Alabama, 1972
Typical smog in Los Angeles, California, in 1940s and 1950s
Aluminum plant (beside church) in New Orleans, Louisiana, 1973
Notes: These are some images from around the United States from days before the Clean Air Act was in place. Our skies looked pretty different 50 years ago, particularly in some urban areas.

## Slide 26: US SO2 and NOx Emissions by Source
Electric utilities are major contributors to acid rain precursors. Source: NAPAP Emissions Inventory, Nov. 1989.

## Slide 27
Mass of sulfur dioxide emissions in the U.S. from 1970 to 2017 (in 1,000 tons)
U.S. sulfur dioxide emissions 1970-2017
Note: United States; 1970 to 2017
Further information regarding this statistic can be found on page 8.
Source(s): Environmental Protection Agency; ID 501303
Chart: Volume of emissions in thousand tons
| 1970 | 1975 | 1980 | 1985 | 1990 | 1995 | 2000 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017
Volume of emissions in thousand tons | 31218 | 28044 | 25926 | 23307 | 23077 | 18619 | 16347 | 14546 | 13123 | 11699 | 10324 | 9089 | 7732 | 6479 | 5079 | 4873 | 4674 | 3685 | 2960 | 2815
5
Coal combustion is the major source
https://www.statista.com/statistics/501303/volume-of-sulfur-dioxide-emissions-us/
(by subscription)
➗10

## Slide 29
Notes: Bhutan

## Slide 30
Mass of nitrogen oxides emissions in the U.S. from 1970 to 2017 (in 1,000 tons)
U.S. nitrogen oxides emissions 1970-2017
Note: United States; 1970 to 2017
Further information regarding this statistic can be found on page 8.
Source(s): Environmental Protection Agency; ID 501284
Chart: Volume of emissions in thousand tons
| 1970 | 1975 | 1980 | 1985 | 1990 | 1995 | 2000 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017
Volume of emissions in thousand tons | 26882 | 26378 | 27080 | 25757 | 25527 | 24955 | 22598 | 20355 | 19227 | 18099 | 16909 | 15772 | 14846 | 14519 | 13879 | 13239 | 12589 | 11843 | 11304 | 10770
5
NOx emissions are primarily from transportation (cars, planes, and trucks) and coal combustion
U.S. NO2 trends (2005-2013): EPA Air Quality System (AQS) data versus improved observations from the Ozone Monitoring Instrument (OMI), Lok N. Lok N. Lamsal, B. N. Duncan, Y. Yoshida, N. Krotkov. K. Pickering.. Streets, Z. Lu, http://dx.doi.org/10.1016/j.atmosenv.2015.03.055
https://www.statista.com/statistics/501284/volume-of-nitrogen-oxides-emissions-us/
➗3

## Slide 31
Notes: why the trends; discussion

## Slide 32
Progress has stalled for primary PM2.5 and VOCs (source of secondary aerosols)
PM2.5 (1000 tons/yr; since 1990)
Chart: Volume of emissions in thousand tons
| 1990 | 1995 | 2000 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017
Volume of emissions in thousand tons | 7560 | 6929 | 7288 | 5592 | 5736 | 5881 | 6014 | 5988 | 5964 | 6100 | 5940 | 5780 | 5381 | 5363 | 5348 | 5331
Chart: Volume of emissions in thousand tons
| 1970 | 1975 | 1980 | 1985 | 1990 | 1995 | 2000 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017
Volume of emissions in thousand tons | 34659 | 30765 | 31107 | 27403 | 24108 | 22042 | 17512 | 17753 | 17902 | 18050 | 17759 | 17593 | 17835 | 18154 | 17872 | 17590 | 16883 | 16701 | 16429 | 16202
VOCs (1000 tons/yr; since 1970)
Note: United States; 1990 to 2017
Further information regarding this statistic can be found on page 8.
Source(s): Environmental Protection Agency; ID 501298
by subscription: https://www.statista.com/statistics/501298/volume-of-particulate-matter-2-5-emissions-us/
➗2
➗1.2

## Slide 33
Notes: Volkwagon ; overturned this year. Obama era bailout.

## Slide 34
Observed and anthropogenic modeled trends in BC and OA.
Trends (μg/m3 per decade) in median annual surface BC and OA concentration
simulated in GEOS-Chem (contours) and observed at IMPROVE sites
D. A. Ridley et al. PNAS 2018;115:2:290-295
©2018 by National Academy of Sciences
Data through 1990 - 2012.
Notes: Observed and anthropogenic modeled trends in BC and OA. (A) Trends (μg/m3 per decade) in median annual surface BC concentration simulated in GEOS-Chem (contours) and at IMPROVE sites with at least 18 y of data (black circles) and at least 10 y of data (white circles) between 1990 and 2012. Model trends are for anthropogenic BC emissions only, derived from the EPA emission inventory. (B) Same as A, but for OA. Model trends are for anthropogenic OA emissions only.

## Slide 35
Premature mortality associated with OA.
The decline in population-weighted OA concentration averaged across the United States (thin black line)
and the trend (thick black line) based on a combination of model and IMPROVE observations.
D. A. Ridley et al. PNAS 2018;115:2:290-295
©2018 by National Academy of Sciences
Notes: Premature mortality associated with OA. The decline in population-weighted OA concentration averaged across the United States (thin black line) and the trend (thick black line) based on a combination of model and IMPROVE observations. The cumulative reduction in premature mortality (in 1,000) resulting from the declining trend in OA (red line) is displayed with the mortality uncertainty resulting from the 1-σ uncertainty in population-weighted PM2.5 and OA estimates (dark gray) and the 1-σ uncertainty when combined with the relative risk uncertainty, determined by Burnett et al. (37) for diseases linked to PM exposure (light gray; SI Appendix). The premature mortality for modeled biogenic SOA (olive), anthropogenic SOA (green), primary OA (blue), and wildfire OA (orange) are shown relative to the estimate based on the combination of model and IMPROVE observations.

## Slide 36: Progress in Implementation
36
Does Not Include CO2
Notes: It is important to balance improvements in the environment with economic prosperity. Students interpret this slide.
In the U.S., we have seen large increases in a number of measures of economic growth, as well as an increase in our overall population, along with increases in energy consumption and transportation demand.
And yet, we have also been able to accomplish large reductions in emissions of air pollutants. This graph shows that from 1970 to 2007, emissions of the six principal pollutants has fallen by 57 percent, while our GDP has increased by over 200 percent.
Note that this graph does not include reductions in CO2, which will be the next big challenge for the coming decades, as we look to reduce CO2 emissions while maintaining our economic growth.
36

## Slide 37
Hours/Day
Days/weeks
Weeks/Months
Aerosols – Roll up
Span of time and space scales for air pollution and atmospheric aerosols
Size matters:
Health effects
Lifetimes
Mechanisms and
Dynamics
Smaller particles are deposited deep in the lungs and travel throughout the body, even inside cells.

## Slide 38
Sulfur emissions in the US have declined 10-fold due to controls and switching from Coal to Natural Gas
for electricity.
Particulate (and other) air pollution in the US was severe in the 1950s—1970s.
The Clean Air Act (1963, 1970, 1995) led to huge improvements.
NOx and aerosol concentrations have gone down by factors of 3 (Organic aerosol) – 10 (Sulfate aerosol).
Lives extended (since 1990) > 200,000
Roll -up