## Slide 1: Solutions to Pollution…
Dilution only works in water
Revisit London Fog Pollution event
Watch the video link on the next slide
Come back with your thoughts on these four items:
How was the problem identified?
What was the solution?
What factors had to be considered when developing a solution?
Was the solution sufficient?

## Slide 2: 1950s London Fog: Watch This!
https://www.youtube.com/watch?v=xajjmbJrfEM
Macbeth “Fair is foul, and foul is fair: Hover through the fog and filthy air”

## Slide 3: 6 Cities Study (Lepeule et al., 2012)
Since 2001 to 2009: Average PM2.5 = <18 g m-3
Linear dose-response to 8 g m-3
Each 10 g m-3 of PM2.5
= 14% increase in risk of all-cause mortality
= 26% increase in cardiovascular mortality
= 37% increase in risk of lung cancer mortality
Survival function (probability)
Years of follow up
London Fog: mg/m3

## Slide 4
How does the atmospheric lifetime of a pollutant affect how it is regulated?
Long-lived (persistent) chemicals can be transported long distances
For many chemical screening regulations, persistence in air is defined as a half-life of > 2 days.
UN Convention to Manage Long Range Transport of Air Pollutants (LRTAP Convention), est. 1979, 34 Member states

## Slide 5: Primary vs secondary pollutants
Definition
  Primary pollutants are emitted directly to the atmosphere by the sources (SO2)
  Secondary pollutants are formed in the atmosphere through chemical processes (O3)
Atmosphere is an oxidizing medium (chemical reactions)
  Fate of pollutants

## Slide 6
6
NAAQS = National Ambient
Air Quality Standards
Ozone: O3
Fine particulate matter: PM2.5
Coarse particulate matter: PM10
Carbon monoxide (CO)
Nitrous dioxide (NO2)
Sulfur dioxide (SO2)
Lead (Pb)
Six Criteria Air Pollutants Regulated under NAAQS (Clean Air Act)
Notes: In addition to reducing emissions of air pollutants, we have also seen progress in reducing pollution in the ambient air that we breathe.
For each of the six principle pollutants, we have seen steady improvements, and in much of the U.S., current air quality is at or well below the standards.
6

## Slide 7
Air Toxics
A story of coal, mercury and ineffective regulations…

## Slide 8: Engineering Solutions to Address Societal Problems
Economy
Environment
Society
Stove Pipe Decisions
Economy
Environment
Society
Pillars of Sustainability
Better
Interconnected
Decisions
G. Foley, US EPA
Learning outcomes:
How to characterize the tradeoffs among economic, societal, and environmental outcomes when designing regulations
Critique EPA’s Regulatory Impact Assessment for HAPs regulations

## Slide 9: Power plants are big emitters and many lacked advanced controls (ca. 2005)
Sources: Portion of pollution -- NEI Trends Data (2009) and IPM (2010) (SO2, NOX); MATS rule modeling platform, based on inventory used for 2005 NATA (Hg); Inventory used for 2005 NATA (other toxics). Percent of units: EPA Base Case v. 4.10 PTR
More than 200 Hazardous Air Pollutants (HAPs) are released by coal-fired utilities
About 50%
of coal-burning units were over 40 years old

## Slide 10
In 1998, EPA concluded that there was a “plausible risk to human health” associated with Hg releases from electricity generating units (EGUs) aka: coal-fired power plants.
This triggered what lawyers call the:
Appropriate and Necessary Finding
i.e., it is appropriate and necessary to regulate emissions (as opposed to arbitrary and capricious)
Statutory Authority:
Clean Air Act
Regulatory Agency: US EPA
Mission: “To protect human health and the environment”
1998
Notes: Utilities/Trade Journals started discussing impending regulations for Hg ca. 1990 after the amendments to the Clean Air Act

## Slide 11
Biden administration put a hold on final decision
to overturn appropriate and necessary finding; eliminating the need to regulate Hg
The rule has been in place since 2011 and plants are already in compliance.

## Slide 12: Mitigating health risks associated with mercury releases from coal-fired utilities
Regulatory background
U.S. electricity sector and pollution control technology costs
Modeled benefits of reducing Hg emissions
Actual changes in energy sector, Hg emissions, concentrations and exposures
Climate change and future trajectories in Hg exposure
Are EPA’s estimated benefits = $4-6M/year and costs = $9B reasonable?

## Slide 13: Key Power Plant Rules Overdue
1990: Clean Air Act Amendments (CAA) required EPA to issue standards to reduce emissions of air toxics, also called hazardous air pollutants (HAPs), from many sources, and to study whether to do so for power plants
  Since then, EPA has issued air toxics standards for most major source categories – but not for power plants
1998: EPA released the Utility Toxics Study Report to Congress
2000: EPA listed power plants for regulation under the CAA air toxics provisions
  EPA determined it was “appropriate and necessary” to regulate emissions of air toxics from power plants, triggering CAA requirements to regulate power plants
  Mercury cited as pollutant of greatest concern but other toxics of potential concern include arsenic, chromium, cadmium, nickel, hydrochloric acid, dioxin/furan
2005: EPA reversed power plant air toxics determination
  EPA determined it was neither “appropriate nor necessary” to regulate emissions of air toxics from power plants and removed those units from the CAA section 112(c) source category list
  EPA issued the Clean Air Mercury Rule (CAMR), which regulated mercury from power plants through a cap and trade program under CAA section 111
2008: DC Circuit Court vacated both EPA's action removing power plants from the section 112(c) source category list and CAMR
2011: EPA issues final standards for MACT rule known as MATS: Mercury and Air Toxics Standards
2016: Supreme Court orders EPA to provide additional justification for the Appropriate and Necessary finding ca. 1998 given the discrepancy between costs ($9Billion) and benefits ($4-6M) listed in EPA RIA
2020: EPA reverses the Appropriate and Necessary finding, repealing MATS. All utilities are already in compliance.
2021: EPA stays the decision – basically asking for more time to decide what to do

## Slide 14: Executive order 12866: Cost-benefit analysis for regulations
In deciding whether and how to regulate
  Assess all costs and benefits of all alternatives
  Include options of not regulating
  Both quantifiable and non-quantifiable measures
Maximize net benefits including:
  Economic, Environmental, Public health and safety, Distributive impacts, Equity
Propose regulation
  “Upon a reasoned determination that the benefits of the intended regulation justify its costs”
  One piece of information to inform the decision-making process
This becomes part of the “Regulatory Impact Assessment” (RIA) that supports each proposed regulation

## Slide 15: Benefits from regulating U.S. Coal-fired Utilities
US EPA (2011)** | Maximum Available Control Technology (MACT) Standards (MATS) | Benefits: $4-6 million per year.
US EPA (2005) | Hg cap under CAIR and CAMR for power plant emissions | Benefits: Less than $168 million per year.
Trasande et al. (2005) | Costs of current Hg emissions from all sources | $9.5 billion per birth cohort $1.4 billion due to power plants
Rice & Hammitt (2005) | Cap of 26 tons and 15 tons on power plant emissions (U.S.) | Benefit: $3.8 - $5.7 billion
**Long list of unquantified benefits = $$ zero for policy-makers

## Slide 16: What information is needed to assess the costs and benefits of utility regulations?

## Slide 17: Mitigating health risks associated with mercury releases from coal-fired utilities
Regulatory background
U.S. electricity sector and pollution control technology costs
Modeled benefits of reducing Hg emissions
Actual changes in energy sector, Hg emissions, concentrations and exposures
Climate change and future trajectories in Hg exposure
Are EPA’s estimated benefits = $4-6M/year and costs = $9B reasonable?

## Slide 18: Electric Power Industry Revenues in Hundreds of Billions/year
$219 billion in annual electricity sales in 2002
Utilities (65% of generation1)
  Investor-owned
  Municipal
  Rural co-ops
  State-owned
  Federal (Tennessee Valley Authority, Bonneville Power Authority, Power Marketing Administrations)
Non-utilities (35% of generation)
  Independent power producers
  Combined heat and power facilities (commercial and industrial)
  Share has grown dramatically - $90 Billion of merchant plant investment in past 5 years
[1] Data from EIA for July 2004

## Slide 19: Most U.S. Electricity Generation From Coal ca. 2002
Electric Generation in 2002
Historical & Projected Electric Generation
Source: 2002 and historical generation is from EIA’s Annual Energy Review. Projected generation is from EPA’s Integrated Planning Model.
Forecast

## Slide 20
Coal Supply Regions
Appalachia (Bituminous)
  Northern
  Central
  Southern
Interior (Lignite and Bituminous)
  North Dakota Lignite
  Gulf Coast Lignite
  Illinois Basin
  Other Western Interior
West (Bituminous and Subbituminous)
  Powder River Basin (PRB)
  Rockies
  Southwest
  Northwest
Regulations try to avoid adversely affecting the economic interests of different regions

## Slide 21: Coal Fired Power Plants in the U.S. ca. 2002
About 1,300 coal-fired generation units (~ 500 coal-fired power plants), representing about 305 GW of generation capacity
Existing Controls:
  Almost all units have particulate matter (PM) control devices
  About one-third of capacity has SO2 scrubbers
  Most have initial NOx controls (low-NOx burners)
  About one-third of the capacity (primarily in the east) will have advanced NOx control (SCR) when NOx SIP call is fully implemented

## Slide 22: We have the technology to virtually eliminate emissions of ALL pollutants from coal-fired utilities– implementation is a matter of cost
PM: ESP=Electrostatic Precipitator, FF=Fabric Filter, Cyclone, Scrubber
SOx: Flue Gas Desulfurization (FGD)
Hg: Activated Carbon Injection (ACI)
NOx: Selective Catalytic Reduction (SCR), Selective Non Catalytic Reduction (SNCR)
Covert NOx into N2 and H2O

## Slide 23
Control Technology Needed to Achieve MATS Standards
Retrofit pollution control installations on coal-fired capacity (by technology) with the base case and with the final MATS, 2015 (measured in GW capacity).
FGD: flu gas desulfurization (scrubber)
DSI: dry sorbent injection
SCR: selective catalytic reduction
ACI: activated carbon injection
FF: fabric filter
Source: Integrated Planning Model run by EPA, 2011

## Slide 24
Modeled effects of MATS on future electricity costs small and within normal historical fluctuations
Total costs of regulations estimated at $9B
This is a small fraction of industry revenue (hundreds of billions)
Costs are passed on to consumers
Effects of MATS are small and projected costs were within the normal historical fluctuation of electricity prices.
Actual costs have been less than $1B/year and were overestimated
This is common in environmental regulations
Sources: EIA Historical (Annual Energy Review – October 2011); EIA Projected (Annual Energy Outlook 2011 ); EPA modeling of projected price increases using the Integrated Planning Model.
Average monthly electric bill would increase by a maximum of $2.71 (0.3 cents per kW hour)

## Slide 25: Mitigating health risks associated with mercury releases from coal-fired utilities
Regulatory background
U.S. electricity sector and pollution control technology costs
Modeled benefits of reducing Hg emissions
Actual changes in energy sector, Hg emissions, concentrations and exposures
Climate change and future trajectories in Hg exposure
Are EPA’s estimated benefits = $4-6M/year and costs = $9B reasonable?

## Slide 26
c
Near-field
deposition
Long range
transport
Hg “HOT SPOT”
far-field
deposition
foreign countries
remote environments
HgII
Hg0
Mercury is a local and global pollutant

## Slide 27
Power Plants were the Largest Remaining Source of Mercury Emissions in the U.S.
Industrial Category | 1990 Emissions tons per year (tpy) | 2005 Emissions (tpy) | % Reduction
Power Plants | 59 | 53 | 10%
Municipal Waste Combustors | 57 | 2 | 96%
Medical Waste Incinerators | 51 | <1 | >98%
Source: EPA’s 2005 NATA Inventory Modified for the Toxics Rule 2005 Base Year (2010)
48% of total Hg emissions in 2015

## Slide 28
Components of Regulatory Impact Assessment (RIA) for Hg Releases from Coal-Fired Utilities
Hg0 (gas)
HgII
CH3Hg (MeHg)

## Slide 29
water
plankton
small fish
big fish
top predators
methylmercury concentration
Concentrations are x106-107 water
Neurotoxicant
Impaired cardiovascular health
Endocrine disruptor
Immunotoxin
104 - 105
Methylmercury is a bioaccumulative neurotoxicant
CH3Hg(I)
Societal Costs of methymercury exposure in US & Europe > $15 B
(Bellanger et al., 2013; Grandjean et al., 2012)

## Slide 30
Mahaffey et al., 2009
Exposure to methyl-Hg is from seafood consumption
Rice exposures in contaminated mining regions in China are a localized problem

## Slide 31
Inorganic Hg includes:
Quicksilver
  0.01% absorption
Hg0 (inhalation)
~70% absorption
HgII
  Avg of 7% absorption (range 1-17%)
Methyl-Hg (CH3Hg or MeHg)
>90% absorption efficiency
Primarily a central nervous system toxin
Half-life of 50-70 days
Chelation not effective
The form of Hg determines its health impact

## Slide 32
Frothing at the mouth
“Excessive” shyness
Source: USGS Fact Sheet
Health Effects Associated with MeHg Exposures

## Slide 33
“After a personal experience with mercury poisoning, Richard Gelfond ’82 (IMAX CEO) established a new fund in the amount of $1 million to improve understanding of environmental cycling and public health effects of mercury.”
Mainly among sushi lovers and/or when canned tuna is consumed in extremely large quantities
http://www.stonybrook.edu/research/news/RN/resnew100512.shtml
Cases of acute toxicity in adults (mercury poisoning)

## Slide 34
Decreasing Credibility
Fetal exposures
>> RfD
Any fetal exposures
Male consumers of non-fatty freshwater fish with high MeHg
Male fish consumers
All fish consumers
Children IQ Deficits
Adult Cardiovascular Effects
EPA’s RfD (2000)
5.8 μg/L blood ~ 1 ppm hair (100,000 – 600,000 US children/year)
EPA chose to only include impacts of methylmercury exposure on IQ in children in their RIA
Rice and Hammitt, 2005
http://books.nap.edu/execsumm_pdf/9899.pdf

## Slide 35
5.8 g/L
EPA’s RfD = 0.1 ug/kg/d (Other countries RfD: 0.1 - 0.47 µg/kg/d )
Based on an uncertainty factor of 10 to protect sensitive groups.
EPA’s RfD (reference dose) is widely believed to be too high – is currently being revisted
There is no evidence of a threshold effect associated with methylmercury exposure
At maternal blood concentrations of 58 g/L blood mercury one would expect a doubling of the number of poor performers on neurodevelopmental tests (from 5% to 10% of the population).
Uncertainty factor of 10 to
protect sensitive groups

## Slide 36
Environmental Health Perspectives
Vol. 119, No. 5, May 2011
Robust evidence for cardiovascular impacts of MeHg Exposure
New England J of Medicine, 2011
Low to moderate fish consumers

## Slide 37
Monetary benefits attributable to cardiovascular health are much large than IQ benefits
CVD Leading Cause of Death for US Adults (>900,000/year)
US: 4.2 million births 240 million adults
Cost: VSL = $7.6M
1AHA, 2004; 2Rice et al., 2010; 3Bellanger et al., 2013; 4Grandjean et al., 2012
VSL = Value of Statistical Life established by the Office of Management and Budget
IQ Benefits
$18,000/IQ point
Cardiovascular
Benefits (~80%)2
Declines in mortality
Cost: 15.8 Billion USD/year3,4
https://www.epa.gov/environmental-economics/mortality-risk-valuation#whatvalue

## Slide 38
Geographic Distribution of Largest Anthropogenic Mercury Emissions Sources in the U.S. (1999) and Canada (2000)
15

## Slide 39
Hg(0)
Hg(II)
Near-field deposition
Long-range transport
oxidation
foreign countries
remote environments
far-field deposition
Hg(II)
reduction
Local “hot spot”
atmosphere
surface
Atmospheric redox chemistry plays key role
in Hg deposition to the surface
39

## Slide 40: Oxidation and reduction reactions shift global deposition patterns
Low concentrations of marine organics
NO2 and HO2, and higher Br
Higher deposition to tropical oceans supported by observed high oceanic Hg0 concentrations in the ITCZ, but no observations of wet deposition to constrain directly
49%
40
Selin et al. (2007)
Horowitz et al. (2017)
Holmes et al. (2010)

## Slide 41
EPA models suggested the majority of Hg emissions from utilities would be transported globally
U.S. EPA Simulations using CMAQ Model 2005
Mercury Deposition Attributable to Utility Emissions
Percent Change in Deposition (associated with a 100% decrease in utility emissions)

## Slide 42
CH3Hg
SEDIMENT/
WATER
microbes
Sulfate/Iron Reducing Bacteria
AIR
Hg(II)
Hg(0)
Hg(II)
Conversion of Hg(II) to CH3Hg drives bioaccumulation

## Slide 43
Advisories for specific water bodies
Statewide freshwater advisory
Statewide freshwater advisory and additional advisories on specific waterbodies.
No mercury advisories
Statewide Coastal Advisories
* Statewide advisory for lakes only
NOTE: This map depicts the presence and type of fish advisories issued by the states for mercury as of December 2010. Because only selected waterbodies are monitored, this map does not reflect the full extent of chemical contamination of fish tissues in each state.
Source: 2010 National Listing of Fish Advisories
http://water.epa.gov/scitech/swguidance/fishshellfish/fishadvisories/upload/nlfa_slides_2011.pdf
Advisories in 2010
Fish Consumption Advisories for Mercury are Everywhere!

## Slide 44
EPA chose to only consider methylmercury exposures for the children of freshwater recreational fishers
Source: EPA RIA, 2005
Most seafood consumed in the US is from the commercial market and marine ecosystems

## Slide 45: Number of Freshwater Recreational Freshwater Anglers very Small Compared to Total Seafood Consumers (>300 million)
Region | Days Fishing (million days) | Percent of Total | Estimated Number of Consumers (millions of people)
Northeast | 37 | 9 | 2.0-4.9
Mid-Atlantic | 3 | 1 | 0.2-0.4
Southeast | 110 | 26 | 5.9-15
Midwest | 151 | 36 | 8.1-20
West | 123 | 29 | 6.6-17
Source: Fish and Wildlife Service, 2002
>90% of the U.S. population reports consuming seafood

## Slide 46
Commercial marine fish consumption is the predominant source of MeHg exposure the United States
82% of Population-Wide MeHg Exposure
from Marine Ecosystems
Sunderland et al., 2018

## Slide 47: Mitigating health risks associated with mercury releases from coal-fired utilities
Regulatory background
U.S. electricity sector and pollution control technology costs
Modeled benefits of reducing Hg emissions
Actual changes in energy sector, Hg emissions, concentrations and exposures
Climate change and future trajectories in Hg exposure
Are EPA’s estimated benefits = $4-6M/year and costs = $9B reasonable?

## Slide 48
Sources of U.S. Electricity Generation
2010
2016

## Slide 49
Hg emissions declines reflect retirements, fuel switching and emissions controls for coal-fired utilities
Source: US EPA, 2019

## Slide 50
Chart: Coal Capacity with Mercury Controls or Co-Controls
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018
ACI | 16.3172 | 18.6422 | 21.6282 | 22.2392 | 33.7865 | 85.4403 | 116.1843 | 113.8853 | 108.5593
SO2 Co-Control only | 166.1961 | 172.2621 | 176.1271 | 179.1471 | 174.1011 | 148.1391 | 136.4511 | 131.9351 | 127.4151
Neither | 170.728 | 162.5433 | 153.0106 | 140.8104 | 125.2695 | 83.5564 | 47.4632 | 40.1307 | 35.3129
Source: US EPA, 2019

## Slide 51
U.S. mercury emissions, major sources 1990, 2005, 2008, 2011
NEI 2011 version 1 2014
246
105
61
52
79% Decrease between 1990-2011
Mercury emissions from coal-fired EGUs declined 86% between 2010 and 2018

## Slide 52: Marked decreases in Hg0 and HgII emissions due to SOx and NOx controls
Zhang et al., 2016
U.S. mercury emissions from the power sector have decreased
65% from 2015-2017 and 81.7% from 2011-2017. TRI 2018
Decline in this component was underestimated by EPA

## Slide 53
We saw a >30% decline in atmospheric Hg concentrations between 1990 and 2010
Observed Trends Atmospheric Hg0 (1990-2010)
Hg0 (ng m-3)
Zhang et al., 2016

## Slide 54
Cross et al. 2015
Decreasing Hg in mid-Atlantic blue fish

## Slide 55: Decreases in mercury in Atlantic bluefin tuna
Decreases
in mercury 2004-2012
Across age classes in
Atlantic bluefin tuna
Lee et al, 2016

## Slide 56: Declines in human exposure in National Health and Nutrition Examination Survey (NHANES)
Blood methylmercury in
U.S. women (16-49) have
declined likely due to
decreases in fish
mercury coupled with
improved consumption
advisories. NHANES 2013
U.S. children born with prenatal exposure exceeding the EPA reference dose have decreases from 200,000-400,000 to 100,000-200,000. EPA 2013

## Slide 57
Source: Mahaffey et al., 2009
Percent of women exceeding U.S. EPA RfD
NHANES Survey Year
U.S. Women Age 16-49 between 1999-2004
Blood Hg levels in women of childbearing age

## Slide 58: Mitigating health risks associated with mercury releases from coal-fired utilities
Regulatory background
U.S. electricity sector and pollution control technology costs
Modeled benefits of reducing Hg emissions
Actual changes in energy sector, Hg emissions, concentrations and exposures
Climate change and future trajectories in Hg exposure
Are EPA’s estimated benefits = $4-6M/year and costs = $9B reasonable?

## Slide 59: What does the future hold?
Appropriate and Necessary finding for MATS reversed (“some pollutants are not worth regulating!”)
Once in, always in rule also being repealed:
Established in 1995, the “once in, always in” policy determined that any facility subject to major source standards would always remain subject to those standards—even if production processes changed or controls were implemented that eliminated or permanently reduced that facility's potential to emit hazardous air pollutants…
Climate change is altering chemical cycling independently of emissions (see tuna example)

## Slide 60
Tuna accounts for almost 40% of
US population-wide methylmercury exposure
Based on NMFS
and FAO data
Decadal differences
2000 – 2010
Sunderland et al., 2018

## Slide 61
Seawater warming affects fish metabolism and growth, MeHg elimination, prey availability, and species habitat
Notes: Mean seawater temperatures increased between 0.5 to 0.7°C between 1900 and 2000, followed by a period of rapid warming of 0.03°C per year beginning in 2004

## Slide 62
Species respond differently to temperature increase
Relative change in MeHg (%) in response to 1°C increase
Average
30%
Max
160%

## Slide 63
Schartup et al., 2019, Nature
~50% Increase
between
1970-2015
>20% decrease
between
1990-2010

## Slide 64: Current plateau in global Hg emissions means seawater warming will be important factor for methylmercury in marine fish
Streets et al., 2019, Atm Environ
Need to reduce both CO2 and Hg emissions!

## Slide 65: How to Download the Data
Air Markets Program Data https://ampd.epa.gov/ampd/
FTP site ftp://newftp.epa.gov/DMDnLoad/emissions/mats/
Field Audit Checklist Tool (FACT) https://www.epa.gov/airmarkets/field-audit-checklist-tool-fact
FACT API https://www.epa.gov/airmarkets/field-audit-checklist-tool-fact-api

## Slide 66: We need stronger not weaker regulations!

## Slide 67
Coal was the most important component of US electricity generation in 2002.
Air Toxics Roll Up: Coal-Fired Utilities
Many air quality regulations have targeted pollution from coal-fired utilities: HAPs, criteria air pollutants (NAAQS), CO2
>200 Hazardous Air Pollutants(HAPs) Released from Coal-Fired Utilities
By 2016, natural gas had replaced coal as the most important fuel used for electricity generation.
Electricity generation from coal has declined because many older, dirty plants have been retired. Remaining utilities have a suite of emissions control devices and came into compliance with MATS between 2015-2017.
We have the technology to virtually eliminate emissions of all pollutants from coal-fired utilities; implementation is a matter of cost and incentives.

## Slide 68
Air Toxics Roll Up: Case Study of Mercury in the Environment
Redox chemistry of Hg (gain of electrons or reduction to Hg0 and loss of electrons to form HgII dictates behavior (deposition or transport) in the atmosphere
Most Hg in ecosystems is HgII. A small fraction is converted by microbes under low oxygen conditions to CH3Hg, the only form of Hg that biomagnifies in food webs.
CH3Hg exposure is a function of how much fish you eat (magnitude) x the [Hg] in fish. This varies ~100x across species and is highest in older, predatory fish like swordfish and tuna
Pregnant women (developing fetus) and children are most vulnerable to neurodevelopmental effects of CH3Hg exposure; Main effect in adults is negative impacts on cardiovascular health.
Shrimp are low in mercury but consumed a lot

## Slide 69
79% Decrease in US Hg emissions 1990-2011
Coal-fired utilities accounted for 48% of US mercury emissions in 2015; largest remaining primary anthropogenic source
Air Toxics Roll Up: Trends in Mercury in the Environment
Large decline in Hg emissions from US coal-fired utilities mainly reflects co-benefits of controls on traditional air pollutants (FGD/SCR)
Declines in Hg emissions explain a 30% decline in atmospheric Hg concentrations observed between 1990-2010. This is much larger than expected when the MATS rule was developed.
Declining Hg concentrations were observed in tuna in the western North Atlantic between 2004-2012 but these levels now appear to be rising due to warming seawater temperatures! Controls on both Hg and CO2 needed!